## Slide 1: Lecture 03: Memory and I/O Modules

## Slide 2
William Stallings Computer Organization and Architecture
Chapter 5
Internal Memory

## Slide 3: Key Content
Memory taxonomy & characteristics
  Physical type, location, capacity, unit of transfer, access method, performance
Memory hierarchy in computer system
  Registers -> Cache -> Main memory -> Disk
RAM organization (SRAM and DRAM)
  Cell -> Array -> Chip
Memory module extension
  Bit & word extension

## Slide 4: Physical Types of Memory
Semiconductor
  RAM & ROM
Magnetic
  Disk & Tape
Optical
  CD & DVD

## Slide 5: Memory Characteristics Comparison
Location
Capacity
Unit of transfer
Access method
Performance
Physical type
Organisation

## Slide 6: Location
CPU
  registers
Internal
  Cache, main memory
External
  Disk, tape, DVD

## Slide 7: Capacity
Word size
  The natural unit of organization
Number of words
E.g., 2M 8-bit, 16M 1-bit
  Same capacity but different organization

## Slide 8: Unit of Transfer
Internal
  Usually a word, governed by data bus width
External
  Usually a block which is much larger than a word
  E.g., the CPU can calculate one addition every cycle, but a memory transfer takes two cycles. With the memory interface width to be 4 words, the CPU can be kept with 100% utilization.

## Slide 9: Addressable unit
Smallest location which can be uniquely addressed
Normally a Byte for internal memory
Cluster on disks

## Slide 10: Access Methods (1)
Sequential
  Start at the beginning and read through in order
  Access time depends on location of data and previous location
  e.g. tape
Direct
  Individual blocks have unique address
  Access is by jumping to vicinity plus sequential search
  Access time depends on location and previous location
  e.g. disk

## Slide 11: Access Methods (2)
Random
  Individual addresses identify locations exactly
  Access time is independent of location or previous access
  e.g. RAM, ROM
Associative
  Data is located based on a portion of its contents rather than its address
  Access time is independent of location or previous access
  e.g. cache

## Slide 12: Performance
Access time: time between presenting the address and getting the valid data
Memory cycle time: time may be required for the memory to “recover” before next access
  Cycle time is access + recovery
Transfer rate: rate at which data can be moved
  Unit: transfer per second (e.g., GT/s)
Transfer bandwidth
  Equals Transfer rate * Transfer unit size
  Unit: byte per second (e.g., GB/s)

## Slide 13: Quiz
Determine the access time, transfer rate, and transfer bandwidth for the following memory
  A memory transfer takes two cycles, and each transfer has 4 bytes
  Clock frequency is 1 GHz

## Slide 14: Semiconductor Memory
The basic element of a semiconductor memory is the memory cell
  exhibit two stable states, representing binary 1 and 0
  capable of being written into to set the state
  capable of being read from to sense the state
RAM (Random Access Memory)
  Misnamed as all semiconductor memory is random access
ROM (Read-Only Memory)

## Slide 15: Memory Basics
RAM: Random Access Memory
  historically defined as memory array with individual bit access
  Refers to memory with both Read and Write capabilities
ROM: Read Only Memory
  No capabilities for “online” memory Write operations
  Write typically requires high voltages or erasing by UVlight

## Slide 16: Memory Basics
Volatility of Memory
  Volatile memory loses data over time or when power is removed RAM is volatile
  non-volatile memory stores date even when power is removed
  ROM is non-volatile
  Static vs. Dynamic Memory
    Static: holds data as long as power is applied (SRAM)
    Dynamic: will lose data unless refreshed periodically (DRAM)

## Slide 17: Random Access Memory (RAM)
Read/Write
Volatile
  must be provided with a constant power supply
Temporary storage
  When the power is gone, data are lost
Static or dynamic
  SRAM or DRAM

## Slide 18: Recap on Digital Circuit
Field effect transistor (FET)
  pFET vs nFET
CMOS gate:
  Complementary metal–oxide–semiconductor
Quiz: what is this gate for?

## Slide 19: Quiz: can you identify those gates?

## Slide 20: Static RAM
Bits stored as on/off switches
No charges to leak
No refreshing needed when powered
More complex construction
Larger per bit
More expensive
Does not need refresh circuits
Faster
For the use of register & cache
traditional flip-flop logic-gate configurations

## Slide 21: Dynamic RAM
Bits stored as charge in capacitors
Charges leak
Need refreshing even when powered
Simpler construction
Smaller per bit
Less expensive
Need refresh circuits
Slower
For the user of main memory

## Slide 22: Key Content
Memory taxonomy & characteristics
  Physical type, location, capacity, unit of transfer, access method, performance
Memory hierarchy in computer system
  Registers -> Cache -> Main memory -> Disk
RAM organization (SRAM and DRAM)
  Cell -> Array -> Chip
Memory module extension
  Bit & word extension

## Slide 23: Memory is Organized with Hierachy
Registers
L1 Cache
L2 Cache
Main memory
Disk cache
Disk
Optical
Tape

## Slide 24: Why Memory Hierarchy

## Slide 25: Idea Behind Memory Hierarchy

## Slide 26: Example
C code

## Slide 27: Key Content
Memory taxonomy & characteristics
  Physical type, location, capacity, unit of transfer, access method, performance
Memory hierarchy in computer system
  Registers -> Cache -> Main memory -> Disk
RAM organization (SRAM and DRAM)
  Cell -> Array -> Chip
Memory module extension
  Bit & word extension

## Slide 28: Memory Interface with CPU
地址 0
1
2
3
4
5
…
…
0x3FF (1023)
内存 Memory (1KB)
CU 控制单元
BX
ALU 运算单元
下条指令
AX + BX -> addr0
AX
BX
addr0
字节 Byte (8 bit比特)
CX
DX
AX
字 word (16/32/64比特)

## Slide 29: Memory Interface with CPU
地址 0
1
2
3
4
5
…
…
0x3FF (1023)
内存 Memory (1KB)
地址 address
字节 Byte (8 bit比特)
数据 data
 | 1K x 8 | 2K x 4 | 8K x 1
Memory Capacity | 1 KB | 1 KB | 1 KB
Data Bus Width | 8 | 4 | 1
Addr Bus Width | 10 | 11 | 13

## Slide 30: Memory Interface with CPU
地址 0
1
2
3
4
5
…
…
0x3FF (1023)
内存 Memory (1KB)
地址 address
字节 Byte (8 bit比特)
数据 data
 | 1K x 8 | 2K x 4 | 8K x 1
Memory Capacity | 1 KB | 1 KB | 1 KB
Data Bus Width | 8 | 4 | 1
Addr Bus Width | 10 | 11 | 13

## Slide 31: Memory Chip
N x n memory chip
  n = chip word width (note that this “word” is chip word not CPU word)
  N = number of n-bit words
Chip I/O
  Data (in and out): Dn-1 – D0
  Address: Am-1 – A0
  Control
    WE = write enable (assert low)
      WE=1: read, WE=0: write
    En block enable (assert low)

## Slide 32: Memory Chip (Logical View)
Example: 4M x 4 RAM (16-Mbit RAM chip)
  222 = 4 M (4x1024x1024) word
  Each word has 4 bits
  22 address lines (reduced to 11 if multiplexed)
  4 data lines

## Slide 33: Memory Chip (Physical View)
Example: 4M x 4 RAM (16-Mbit RAM chip)
A 16Mbit chip has 16M SRAM cells
But how are they organized?
Is this
4M x 4 array
a good organization?

## Slide 34: Memory Array
NR x NC array of 1-bit cells
  NR = number of rows
  NC = number of columns

## Slide 35: Memory Chip (Physical View)
A 16Mbit chip can be organised as 1M of 16-bit words
A 16Mbit chip can be organised as a 2048 x 2048 x 4bit array
  Reduces number of address pins
    Multiplex row address and column address
    11 pins to address (211=2048)
    Adding one more pin doubles range of values so x4 capacity

## Slide 36: Typical 16 Mb RAM (4M x 4)
The 4M x 4 RAM is organized as four 2048 x 2048 array

## Slide 37: How to Access Memory Array

## Slide 38: How to Access Memory Array
Example of 4 x 1 array
Example of 16 x 1 array

## Slide 39: How to Access Memory Array
Example of 4 x 1 array
Example of 16 x 1 array

## Slide 40: Key Takeaway in This Part
Understand the logical interface for a memory chip
Understand the internal organization of the chip

## Slide 41: Key Content
Memory taxonomy & characteristics
  Physical type, location, capacity, unit of transfer, access method, performance
RAM organization (SRAM and DRAM)
  Cell -> Array -> Chip
Memory hierarchy in computer system
  Registers -> Cache -> Main memory -> Disk
Memory module extension
  Bit & word extension

## Slide 42: Module Organisation
To organize a memory module：
If the module needs bigger unit of transfer than that of given memory chips, bit extension
Every chip has the same address space
A memory module consisting of 256K 8-bit words, using 8 256K1-bit chips

## Slide 43: Bit Extension Example
You have 256K1-bit RAM chips. How can you build a memory module of 256 KB (with word size of 8 bits) and how to connect this module with a computer system?
D7~D0
A17-0
D7
A17~A0

## Slide 44: Bit Extension Example
You have 256K1-bit RAM chips. How can you build a memory module of 256K32-bit and how to connect this module with a computer system?
A17-0
A17-0
What if the addressable unit is byte?

## Slide 45: Module Organisation (2)
To organize a memory module：
If the module needs larger number of words than that of given memory chips, word extension
Chips in different group has different address range
A memory consisting of 1M8-bit words, having four groups of chips

## Slide 46: Word Extension Example
You have 256K8-bit RAM chips. How can you build a memory module of 2M8-bit and how to connect this module with a computer system?

## Slide 47: Quiz
You have 128K8-bit RAM chips. How can you build a memory module of 128K16-bit and how to connect this module with a computer system?
A17-1
D15~D0
D7
A17~A0
128K
8
D15~D8
128K
8
D7~D0
A17-1

## Slide 48: Word and Bit Extension Example
Now you have 256K8-bit RAM chips. How can you build a memory module of 2M32-bit and how to connect this module with a computer system if the addressable unit is byte?

## Slide 49: Memory Module Extension Summary
CPU Word
  The size of instruction operand 一条指令中数据的宽度
  Add AX, BX, CX (Size of register AX/BX/CX)
CPU addressable unit
  The size of data represented by an address
  Usually one byte (8 bits)
Memory chip N x n
n: size of memory word
N: number of words
Interface
Address bus width
Data bus width
Control
Data
Addr
Notes: 接口

## Slide 50: Memory Module Extension Summary
When to use word/bit extension
  CPU wants the memory module of NCPU x nCPU
  Memory chip has Nmem x nmem
Word extension: NCPU > Nmem
  Connect data bus of CPU and all memory chips directly
  Requires extra decoder for address bus connection
Bit extension : nCPU > nmem
  Connect address bus of CPU and all memory chips directly
    May discard some address lines when nCPU > CPU addressable unit
  Assemble memory chips’ data buses to connect with CPU

## Slide 51: Quiz
For a 1MB memory module
  If addressable unit equals 8，What’s the address range
  If addressable unit equals 32，What’s the address range
If we have 256K x 4bit memory chip
  If data bus width = 8，how do we extend?
  If data bus width = 32，how do we extend?
0x00000-
0xFFFFF
0x00000-
0x3FFFF
CPU wants 1M x 8:
(1M/256K)x(8/4)=4x2
4 times word extension and 2 times bit extension
CPU wants 256K x 32: (256K/256K)x(32/4)=1x8
8 times bit extension
(need to discard address A0-A1lines)

## Slide 52: Read Only Memory (ROM)
Permanent storage
Nonvolatile
  Needs no power
Normal applications of ROM (Firmware)
  Library subroutines
  Systems programs (BIOS)
  Function tables

## Slide 53: Types of ROM
Written during manufacture
  Very expensive for small runs
Programmable (once)
  PROM
  Needs special equipment to program
Read “mostly”
  Erasable Programmable (EPROM)
    Erased by Ultraviolet radiation
  Electrically Erasable (EEPROM)
    Takes much longer to write than read
  Flash memory
    Erase whole memory electrically

## Slide 54: Key Content Review
Memory taxonomy & characteristics
  Physical type, location, capacity, unit of transfer, access method, performance
RAM organization (SRAM and DRAM)
  Cell -> Array -> Chip
Memory hierarchy in computer system
  Register -> cache -> main memory -> disk
Memory module extension
  Bit & word extension

## Slide 55: So you want fast?
It is possible to build a computer which uses only static RAM (cache)
This would be very fast
This would need no cache
  How can you cache cache?
This would cost a very large amount
Trade-offs among speed, capacity, and cost

## Slide 56: Assignment Two
Now you have 128K-bit RAM chips. How can you build a memory module of 1M-bit and how to connect this module with a computer system if the addressable unit is byte?
  Draw the address/data lines according to the example in the slides